## Slide 1: Cosmos
Tailoring cosmos for use with fprime deployment applications

## Slide 2: Overview
COSMOS – Open source system to interface embedded system commanding and telemetry-monitoring
Generalized and extendable to connect to anything from test equipment to development boards or satellites
  Included support for TCP/IP Sockets, Serial, or UDP Socket interfaces
  Custom interfaces possible
Functionality similar to Fprime’s GSE (a.ka. GDS)
Fprime COSMOS configuration generated from Fprime XML
  No unit conversion currently supported
  Variable length command arguments not supported (i. e. String’s, etc.) – a COSMOS issue

## Slide 3: Overview cont.
Target = Fprime Deployments (e.g. target embedded application)
Each target has an interface within Cosmos to send and receive telemetry
Support EVR’s and channels, but no difference inside of COSMOS – both generalized as telemetry
  Telemetry Screens for monitoring channels
  Data Viewer app for monitoring EVR’s
Support for Commanding
Notes: Label screen shot. Also perhaps animate the parts.

## Slide 4: Tools
Suite of built-in applications that send commands and monitor telemetry
Command and Telemetry Server application communicates with the other applications via JSON messaging
New apps can be built using COSMOS API and JSON communication
Notes: Label screen shot. Perhaps stuff about apps from last slide belongs on this slide.

## Slide 5: configuration
Cosmos targets, interfaces, and tools all configured in text files using COSMOS API
Cosmos installed via gem install, demo built by command “cosmos demo DIR_NAME”
Main uses: specifying contents of cmd, tlm packets, creating interface, setting paths for tools to find target configurations

## Slide 6: Configuration cont.
Support for multi-string telemetry but not commands, support all Fprime data types and serializables
Embedded ruby capability to reuse text
Servers, write protocols and read protocols link to Ruby scripts allowing for custom creation
Notes: A slide for command sender, data viewer and telemetry viewer. Screenshot of each, example text config snippet for each. And descriptive words.

## Slide 7: CONFIGURATION CONT.
Controls EVR display
Allows multi string tlm packets
Drops first 13 bits Ref app sends
Adds /targets directories to cosmos path
Defines channel screen
Partial add-on
EVR view config
Interface config
Reference to scripts in /lib
Adds directories to cosmos path
Contains definitions of cosmos tlm and cmd. Each directory also contains a partial file with packet header arguments
Config files for every tlm packet item

## Slide 8: Generator tool overview
Tool takes Topology XML as input, and generates all necessary config files to add deployment targets, interfaces, and commands, EVRs, Channels configuration to Cosmos
Tool reused the Fprime (codeGen.py) XML parsing classes
Cheetah templates for each config file that is generated
Cosmosgen.py is added to Autocoders/bin, cosmos package added to Autocoders/src/utils
Installation for Ref application (or deployment) target
  Execute ”cosmos demo DIR_NAME”
  Execute “run_cosgen.sh ../../Ref/Top/…
  Execute the COSMOS server by executing CmdTlmServer
  Execute the Ref as “./Ref –p 5000 –a 127.0.0.1”
Notes: Last bullet really belongs in demo slide.

## Slide 9: Generator tool structure
Creates writers and calls their write() method
Parses data from XMLParser and creates models
Contain constants for the deployment
Contain packet data used by .tmpl files
main()

## Slide 10: demo
Install cosmos demo via command “cosmos demo DIR_NAME”
Connect COSMOS server to Fprime Ref app client
Run cosmosgen Tool and connect to Fprime
Demonstrate commands, telemetry in views
Remove other targets
Demonstrate grapher, extractor
Notes: Also summary…