## Slide 1
FPrime Zmq Server
David Kooi
FPrime GSE Server Redesign

## Slide 2: My Work at JPL
Designed new FPrime GSE Server
  Uses ZeroMQ middleware
    Cross platform, high-performance, asynchronous, distributed messaging library.
  Supports reconnect capability
  Supports protocol translation
  Supports multi-target communication
  Updated GSE GUI for use with ZMQ and maintained backwards compatibility with legacy TCP Server
  Tested for server integrity and throughput
Implemented C++ Zmq Radio component within FPrime
  Emulates a radio connection between a flight target and the GSE Server
  Prevents embedded flight target from hanging up on disconnections from GSE.
Overview of summer work
Notes: ZMQ – Fun fact, it is used by CERN’s Remote Device Access library where they need to connect thousands of data points from around the collider
Reconnect capability – Allow clients to arbitrarily connect and disconnect. Pervious server had issues with this.
Protocol Translation – FPrime GSE works with native Fprime packets. Inline protocol translation allows the Fprime ground system to be data agnostic.
Multi target - ZMQ allows many to many communication. The server provides single point communication support for sets of satellites or sets of test equipment.
Updated GSE GUI – It is important to provide backwards compatibility. The Fprime GSE GUI works with the legacy TCP server and the new ZMQServer.
Server Tests: Created a test framework for these two sets of tests.
Server Integrity – Two things: tested that the server could withstand abrupt disconnections. Tested data integrity. Need to ensure that no packets are dropped during operation.
Throughput - Tested throughput with various configurations of publishers and subscribers. Server can achieve 2mb/s.

## Slide 3: Use Cases
Near-term:
  JPL’s Formation Flying Testbed
    Enable multi-target communication
  DoD Testbed configuration
Far-term:
  Constellations of satellites
http://www.satellitetoday.com/newspace/2017/05/24/roccor-exec-supporting-900
-satellite-leo-constellation/
https://www.jpl.nasa.gov/news/news.php?feature=2985
Notes: Formation Flying Testbed: Multiple robots streaming telemetry and receiving commands. Allows central control of the communication’s datapath
DoD testbed: Flight hardware running in parallel with a hardware simulation. Before the datapaths were separate. Now data paths go through one point.
Constellations: Have a university with 3 satellites. Instead of managing three servers, three telemetry databases, there is one server, one database with still the capability for individual spacecraft operation.

## Slide 4: Design Process
Overview
Requirements
Analysis
Design
Implementation
Test
  This design process was followed for both the GSE ZmqServer task and the
  Zmq Radio component task

## Slide 5: Design Process
GSE ZmqServer Requirements
Requirements
Analysis
Design
Implementation
Test
Single point of initial connection
  Client registration on a single port
  Enable Publish Subscribe configuration and inspection
Publish Subscribe Architecture
  Enable multi flight target to multi ground client communication
Robust client connections
  Server should be able to withstand random client disconnection and reconnection
Protocol Translators
  Server shall be able to communicate over protocol barriers
GSE UI Compatability
  Adapt GSE UI for Zmq communication while maintaining backwards compatibility to legacy server.

## Slide 6: Design Process
GSE ZmqServer Analysis
Requirements
Analysis
Design
Implementation
Test
Became familiar with ZMQ
Learned common design patterns
  ZMQ Request-Reply
  ZMQ Pub-Sub
  ZMQ Router-Dealer
Implemented those patterns in simple exercises

## Slide 7: Design Process
GSE ZmqServer Design
Requirements
Analysis
Design
Implementation
Test
Held initial design meetings to discuss design options
Formulated a design on paper
Held further design meetings to discuss viability

## Slide 8: F-Prime Server Overview
Class Diagram
Server
ZmqKernel
AdapterBase
Composed of
Routing Table
Flight Subscriber Thread
Ground Sublisher Thread
n Flight Pubscriber Threads
n Ground Publisher Threads
Event Reactor
Uses
AdapterImpl_1
AdapterImpl_n
Subclasses

## Slide 9: Server Architecture
ZmqServer
Using native FPrime
Ground
Client 1
R
D
D: zmq dealer socket
R: zmq router socket
Cmd/Status
(R)
ZMQ Kernel
R
R
Ground
Client n
R
D
Flight
Client 1
R
D
Flight
Client n
R
D
DEALER
DEALER
DEALER
DEALER
D
D
D
D
Arbitrary Protocol
Native FPrime
Static Subscription sockets receive all incoming packets
Dynamic Publisher sockets.
One thread per connection.

## Slide 10: Server Architecture
ZmqServer
Using Adapters to decode
Ground
Client 1
R
D
D: zmq dealer socket
R: zmq router socket
Cmd/Status
(R)
ZMQ Kernel
R
R
Adapters run as their
Own process
Ground
Client n
R
D
Flight
Client 1
R
D
Flight
Client n
R
D
DEALER
DEALER
DEALER
DEALER
Adapter
R
D
D
R
D
D
D
D
Adapter
R
D
D
R
Arbitrary Protocol
Native FPrime

## Slide 11: Server Architecture
ZmqServer
Using Adapters to encode
Ground
Client 1
R
D
D: zmq dealer socket
R: zmq router socket
Cmd/Status
(R)
ZMQ Kernel
R
R
Adapters run as their
Own process
Ground
Client n
R
D
Flight
Client 1
R
D
Flight
Client n
R
D
DEALER
DEALER
DEALER
DEALER
Adapter
R
D
D
R
D
D
D
D
Adapter
R
D
D
R
Arbitrary Protocol
Native FPrime

## Slide 12: Server Architecture ZMQ Kernel
Command/Status Port
(ROUTER)
Ground-Client Commands
Server Response
Main Event Loop
Ground-Client Side
Flight-Client Side
Flight-Client and Ground-Client
communication
Is symmetrical
Ground-Client Registration
Flight-Client Registration
Server Response
1 publisher thread per client
Runtime
Configurable routing through subscription and subscription commands.
Routing Table
Client
registration creates a new publisher entry in the RoutingTable and creates a new Publisher thread
PUB
Routing Table Command Socket tells publisher threads who to receive messages from
ZMQ
Internal Routing
ROUTER
Flight-Client Subscriber Thread
PUB
Ground-Client Publisher Thread
SUB
DEALER
1 flight subscriber thread
Ground-Client Publisher Thread
SUB
DEALER
Ground-Client Publisher Thread
SUB
DEALER
ROUTER
Ground-Client Subscriber Thread
PUB
Flight-Client Publisher Thread
SUB
DEALER
Flight-Client Publisher Thread
SUB
DEALER
Flight-Client Publisher Thread
SUB
DEALER
1 ground subscriber thread

## Slide 13: Design Process
GSE ZmqServer Implementation
Requirements
Analysis
Design
Implementation
Test
Main ZmqServer work
Included Protocol translation work
Included GSE UI ZMQ adapter and backwards compatibility work

## Slide 14: Design Process
GSE ZmqServer Testing
Requirements
Analysis
Design
Implementation
Test
Server integrity testing
  Given random client connections and disconnections the server stays running
  Tests for packet loss
Throughput testing
  Monitor and record throughput given variable Publish Subscribe configurations and variable packet sizes >2 MB/s*

## Slide 15: Design Process
Zmq Radio Component Requirements
Requirements
Analysis
Design
Implementation
Test
Zmq Radio shall be an active component
Zmq Radio Component shall attempt reconnection with the server if disconnected
Zmq Radio Component shall remain stable while disconnected

## Slide 16: Design Process
Zmq Radio Component Analysis
Requirements
Analysis
Design
Implementation
Test
Reviewed existing ground socket interface component
Reviewed FPrime active component specifications

## Slide 17: Design Process
Zmq Radio Component Design
Requirements
Analysis
Design
Implementation
Test
Design heavily driven by requirements

## Slide 18: Design Process
Zmq Radio Component Implementation
Requirements
Analysis
Design
Implementation
Test
Main work for the Zmq Radio Component

## Slide 19: Design Process
Zmq Radio Component Testing
Requirements
Analysis
Design
Implementation
Test
One unit test to verify state changes
Functional end-to-end inspection

## Slide 20: Demo Overview
Multi-target datapath with SpacePacket translation
Ground
Client 1
R
D
Ground
Client n
R
D
Flight
Client 1
R
D
Flight
Client n
R
D
DEALER
DEALER
DEALER
DEALER
ZmqServer
R
R
D
D
D
D
SpacePacket
SpacePacket
F’ Packet
F’ Packet
D: zmq dealer socket
R: zmq router socket

## Slide 21: What I learned
Experience with the full design cycle
  Requirements, Analysis, Design, Implementation, Test
Learned how flight qualified code is developed
  Multiple design and code reviews for the zmq-radio C++ component
Learned standard documentation procedures
Good experience using and building with ZMQ middleware
Notes: Full Design cycle – It was useful to iteratively design the server. Since was new to ZMQ one design path would need to back up and be reanalyzed.
The full timers were very helpful in considering design challenges and approaches.
Flight qualified code: We had several code reviews for the zmq-radio. It was useful to see flight qualified code in practice.
Documentation Procedures: Learned the Fprime markdown format for design documents. I like the presentation and will take the method back to our cube sat team.
Good experience working on a distributed system. I became more comfortable working with multithreaded and multiprocess applications. I am glad to have learned one distributed messaging library because this make it easier to learn others in the future. =

## Slide 22: Conclusion
Learned a lot this summer
  Much can be taken back to school
  Concrete steps towards becoming a better engineer
Thank you: Len Reder for guidance throughout the project. Garth Watney for help with the FPrime tool suite Tim Canham for FPrime design and library support Brian Campuzano for frequent development input
Notes: Back to school: Fprime is open source. We are looking into using the framework for our C&DH subsystem. This means there is a possibility the server will be used at our school.
Better engineer: Became more familiar with the design process. Learned a new messaging technology. The scope of the task required extensive documentation. This exercised my information presentation ability. Very glad to have been here.