## Slide 1
Cosmos
Tailoring cosmos for use with Fprime deployment applications
Date: 6/28/2018
Jordan Ishii: jordanishii1@gmail.com

## Slide 2: Outline
COSMOS – open source system to interface embedded system commanding and telemetry-monitoring
Built-in tools to send commands, receive and display EVR and channel telemetry
Interface, tools configured via text files and customized with Ruby scripts, Ruby API, and JSON communication
cosmosgen.py generator tool uses Topology XML files to create the necessary config files to add a deployment’s command and telemetry data to COSMOS

## Slide 3: Cosmos Overview
Generalized and extendable to connect to anything from test equipment to development boards or satellites
  Included support for TCP/IP sockets, serial, or UDP socket interfaces
  Custom interfaces possible
Functionality similar to Fprime’s GSE (a.ka. GDS)
Fprime COSMOS configuration generated from Fprime Topology XML
  No unit conversion currently supported
  Variable length command arguments not supported (i.e. strings, etc.) – A COSMOS issue

## Slide 4: Overview cont.
Target = Fprime deployments (e.g. target embedded application)
Each target has an interface within COSMOS to send and receive telemetry
Support EVR’s and channels, but no difference inside of COSMOS – both generalized as telemetry
  Telemetry screens for monitoring channels
  Data viewer app for monitoring EVR’s
CmdTlmServer Application
Displays errors and all incoming tlm and commands
Displays modal window with all incoming / outgoing hex
Option to view raw data for only a certain tlm or cmd packet

## Slide 5: Tools
Suite of built-in applications that send commands and monitor telemetry
Other utility applications:
  Binary file reader (Telemetry Extractor, Table Manager)
  Script runner, Test runner
  Text editor for config files with documentation and syntax completion (Config Editor)
  Long term trending database on top of PostgreSql database integrated within all viewer apps to simulate certain time ranges (DART)
Launcher Application
Notes: Say that we’ll cover the telemetry viewer and commanding apps later

## Slide 6: Tools
Command sender
May alter argument values from middle column
May use api in command history text box to resend commands
TLM Viewer
Uses ruby version of graphics library qt
May customize with graphs, user input, formatted text
Data Viewer
Writes plain text – cannot customize style
Configure views using ruby script

## Slide 7: configuration
COSMOS targets, interfaces, and tools all configured in text files using COSMOS API
COSMOS installed via gem install, demo built by command “cosmos demo DIR_NAME”
Main uses: specifying contents of cmd, tlm packets, creating interface, setting paths for tools to find target configurations

## Slide 8: Configuration cont.
Support for multi-string telemetry but not commands, support all Fprime data types and serializables
Embedded ruby capability to reuse text
Servers, write protocols and read protocols link to ruby scripts allowing for custom creation
Command Config
Server Interface Config

## Slide 9: CONFIGURATION CONT.
Controls EVR display
Allows multi string tlm packets
Drops first 13 bits Ref app sends
Adds /targets directories to cosmos path
Defines channel screen
Partial add-on
EVR view config
Interface config
Reference to scripts in /lib
Adds directories to cosmos path
Contains definitions of cosmos tlm and cmd. Each directory also contains a partial file with packet header arguments
Config files for every tlm packet item

## Slide 10: Generator tool overview
Tool takes topology XML as input, and generates all necessary config files to add deployment targets, interfaces, and commands, EVR’s, channels configuration to cosmos
Tool reused the Fprime (codegen.py) XML parsing classes
Cheetah templates for each config file that is generated
cosmosgen.py is added to Autocoders/bin, cosmos package added to Autocoders/src/utils
Installation for Ref application (or deployment) target
  Execute ”cosmos demo DIR_NAME”
  Execute “run_cosmosgen.sh –p PATH ../../Ref/Top/RefTopologyAppAi.xml”
  Execute the COSMOS server by executing CmdTlmServer
  Execute the ref as “./Ref –p 5000 –a 127.0.0.1”

## Slide 11: Generator tool structure
Write Cheetah templates to .txt and .rb file
Parses data from XMLParser and creates models
Manages filesystem and creates writers
Contain packet data used by .tmpl files
main()
Codegen.py
Generator
Parser
Writers
Models

## Slide 12: Summary
COSMOS sends commands, receive and display EVR and channel telemetry Fprime’s GSE
Config text files control COSMOS functionality – extendable through Ruby API and JSON communication
cosmosgen.py creates config files in a variable directory path, can remove targets after they are created
Structure of tool -> highest-level: cosmosgen | mid-level: generator, parser | lowest-level: models, writers

## Slide 13: demo
Install COSMOS demo via command “cosmos demo DIR_NAME”
Connect COSMOS server to Fprime ref app client
Run cosmosgen tool and connect to Fprime
Demonstrate commands, telemetry in views
Remove other targets
Demonstrate grapher, extractor