## Slide 1
Cosmos
Tailoring cosmos for use with Fprime deployment applications
Date: 6/28/2018
Jordan Ishii: jordanishii1@gmail.com

## Slide 2: Outline
COSMOS – open source user interface that connects to embedded systems
Built-in tools to send commands, receive and display telemetry
COSMOS configured and customized via text files
  Some optional Ruby API code maybe needed
cosmosgen.py generator tool uses Fprime topology XML to create the necessary configuration files for COSMOS to handle Fprime command and telemetry data

## Slide 3: Cosmos Overview
Generalized and extendable to connect to anything from test equipment to development boards or satellites
  Included support for TCP/IP sockets, serial, or UDP socket interfaces
  Custom interfaces possible
Functionality similar to Fprime’s GSE (a.k.a. GDS)
Fprime COSMOS configuration generated from Fprime Topology XML
  No unit conversion currently supported
  Variable length command arguments not supported (i.e. strings, etc.) – A COSMOS issue
  Not yet supporting complex serializable telemetry channels (this is coming)
  Not yet tested on a Linux platform but should work

## Slide 4: Overview cont.
Target = Fprime deployments (e.g. target embedded application)
Each target has an interface within COSMOS to send and receive telemetry
  REF_INT shown is the Fprime Ref app
Support EVR’s and channels
  Both generalized telemetry within COSMOS
  Telemetry screens for monitoring channels
  Data viewer app for monitoring EVR’s
CmdTlmServer Application
Displays errors and all incoming tlm and commands
Displays modal window with all incoming / outgoing hex
Option to view raw data for only a certain tlm or cmd packet

## Slide 5: Tools
Suite of built-in applications that send commands and monitor telemetry
Other utility applications:
  Binary file reader (Telemetry Extractor, Table Manager)
  Script runner, Test runner
  Text editor for config files with documentation and syntax completion (Config Editor)
  Long term trending database on top of PostgreSql database integrated within all viewer apps to simulate certain time ranges (DART)
Launcher Application
Notes: Say that we’ll cover the telemetry viewer and commanding apps later

## Slide 6: Tools
Command sender
May alter argument values from middle column
May use api in command history text box to resend commands
TLM Viewer
Uses ruby version of graphics library qt
May customize with graphs, user input, formatted text
Data Viewer
Writes plain text – cannot customize style
Configure views using ruby script

## Slide 7: configuration
COSMOS installed via Ruby’s “gem install” command
The default configuration generated by the command “cosmos demo DIR_NAME”
COSMOS has specific configuration text files to adapt it to any embedded target:
  Interface/Protocol files
  Command packet files
  Telemetry (channel, EVR) packet files
  Tools configuration files

## Slide 8: Configuration cont.
Servers, write protocols and read protocols link to ruby scripts allowing for custom creation
Support for multi-string telemetry but not commands, support all Fprime data types and serializables
Header files for commands and telemetry created using syntax <%= %>
Command Config
Server Interface Config

## Slide 9: Configuration cont.
EVR Config
Comments contain extra data from XML file
Link to header file
EVR argument data contain name and type
”Derived” items not in packet sent from target

## Slide 10: Configuration cont.
Channel Screen Display Config
Settings change color and size of screen
Layouts include Vertical, Horizontal, Matrix
Any telemetry data can be put in Value widget

## Slide 11: CONFIGURATION CONT.
Controls EVR display from Data Viewer app
Allows variable-length tlm packets
Drops first 13 bits Ref app sends
Adds /targets directories to cosmos path
Defines channel screen
Partial add-on
EVR view config
Interface config
Reference to scripts in /lib
Adds target tool directories to cosmos path
Contains definitions of cosmos tlm and cmd. Each directory also contains a partial file with packet header arguments
Config files for every tlm packet item

## Slide 12: Generator tool overview
Tool takes topology XML as input, and generates all necessary config files to add deployment targets, interfaces, and commands, EVR’s, channels configuration to COSMOS
Tool reused the Fprime (codegen.py) XML parsing classes
Cheetah templates for each config file that is generated
cosmosgen.py is added to Autocoders/bin, COSMOS generator package added to Autocoders/src/utils
Installation for Ref application (or deployment) target
  Execute ”cosmos demo DIR_NAME”
  Execute “run_cosmosgen.sh –p PATH ../../Ref/Top/RefTopologyAppAi.xml”
  Execute the COSMOS server by executing CmdTlmServer
  Execute the Ref App as “./Ref –p 5000 –a 127.0.0.1”

## Slide 13: Generator tool structure
Write Cheetah templates to .txt and .rb file
Parses data from XMLParser and creates models
Manages filesystem and creates writers
Reused from Fprime codegen.py
main()
Codegen.py
Generator
Cosmos Parser
Writers
XML Parsers
Models

## Slide 14: Summary
COSMOS sends commands, receive and display EVR and channel telemetry
Config text files control COSMOS functionality – extendable through Ruby API and JSON communication
cosmosgen.py generates config files
  Certain files optionally edited
Tool structured with models as go-between for Writers and Parsers

## Slide 15: demo
Install COSMOS demo via command “cosmos demo DIR_NAME”
Connect COSMOS server to Fprime ref app client
Run cosmosgen tool and connect to Fprime
Demonstrate commands, telemetry in views
Remove other targets
Demonstrate grapher, extractor